## Slide 1: Classification and update of Land Use data: a multi-source and multi-modal machine learning approach
Martin CUBAUD
PhD director: Ana-Maria OLTEANU-RAIMOND
Supervisors: Arnaud LE BRIS, Laurence JOLIVET
January 16th, 2026
Reviewer: Alexis COMBER, Professor, School of Geography, University of Leeds
Reviewer: Alexander ZIPF, Professor, Heidelberg Institute for Geoinformation Technology
Examiner: Cidália FONTE, Professor, University of Coimbra, INESC Coimbra
Examiner: David SHEEREN, Professor, INP-ENSAT, UMR 1201 Dynafor
Notes: Good afternoon. Dear members of the jury, thank you for attending at my phd defense entitled …

## Slide 2: Introduction
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 3: Context
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: The context of this research work is the need of accurate and up-to-date LU data. These data describes the socio-economic human activities in a given territory, with classes such as agriculture or residential

## Slide 4: Context
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: Alongside with LC data which is a physical description of the territory, with classes such as built-up or vegetation

## Slide 5: Role of LU and LC data
Introduction
State of the art
LU classification
Conclusion
LU change detection
©sdg.un.org
Notes: LU and LC data are used to support several united nation sustainable development goals, such as

## Slide 6: Role of LU and LC data: example of land take
LULC data
Monitoring the evolution and assessing the impact
Defining and monitoring urban planning policies
Objective of zero net land take by 2050 (EU soil strategy, "ZAN" law in 2021)
Introduction
State of the art
LU classification
Conclusion
LU change detection
Bocquet (2023)
Both LU and LC are needed
Notes: For instance, a key role of LULC data is related to the mitigation of Land take. Land Take has several negative impacts on CO2…

## Slide 7: Examples of LULC products
1990
Global dynamic Land Cover 11 LC classes Resolution: 10m Automatic
Every year
2006
2018
2020
2013
Introduction
State of the art
LU classification
Conclusion
LU change detection
EU/Global
France
CORINE Land Cover
44 LULC classes
MMU: 25 ha
Semi-automatic
Every 6 years
Urban Atlas 27 LULC classes MMU: 0.25 ha to 1 ha
Semi-automatic
Every 6 years
2020
OCS GE (IGN) 14 LC x 20 LU classes MMU: 0.05 ha to 0.25 ha
Semi-automatic
Every 3 years
→ Automatic
→ 1
Theia OSO Inglada et al. (2018)
24 (mostly) LC classes Resolution: 10m raster
Automatic
Every year
🧪
OSMLanduse Schultz et al. (2025) 13 LULC classes Resolution: 10m or <1m Automatic
🧪
🧪: Research product
Separation of LU and LC
INSPIRE directive (2007)
Notes: And so, several LULC products have been proposed through the years. For example
Overall, this timeline shows an evolution towards higher resolution, more frequent update thanks to automatization
Among these products

## Slide 8: Life cycle of LULC data
Five main processes in the life cycle of LULC data (OntoLULC-SOTA ontology)
Two challenging subprocesses for LU:
Automatic LU classification
Automatic LU change detection
Introduction
State of the art
LU classification
Conclusion
LU change detection
Cubaud et al. (submitted)
Management
Notes: These LULC products have a life cycle, composed of 5 main processes that were defined in a collaborative ontology research work on LULC in which I participated in the design and instantiation. These five main processes are: We identified…

## Slide 9: Challenge of LU classification
Automatic Land Cover thanks to progress in deep learning (Ma et al., 2019)
Land Use cannot be determined from remote sensing data only (Comber et al., 2005)
Land Cover:
Built-up
Land Cover:
Built-up
Land Use:
Tertiary production
Land Use:
Residential
BD ORTHO © IGN 2020
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 10: Objectives
Automatic LU change detection
Automatic LU classification
To produce LU maps
To update LU maps
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 11: Outline
Introduction
State of the art
Land Use classification
Land Use change detection
Conclusion
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 12: State of the art
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 13: Confusion between Land Use and Land Cover
  Among 361 LU classification articles (systematic analysis 2013 to 2023)
  21% of them actually classify Land Cover
  33% of them mix in their nomenclature LU and LC classes.
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 14: State of the art – LU classification
Introduction
State of the art
LU classification
Conclusion
LU change detection
On actual LU classification articles
Focus on 3 aspects:
Input data sources
Mapping units
Methods

## Slide 15: State of the art – LU classification
Use of a wide variety of:
Data sources:
  Remote sensing imagery
  Points of Interest
  Topographic data
  Land Cover data
  …
The use of several data sources improves the classification
Introduction
State of the art
LU classification
Conclusion
LU change detection
©BD Ortho
©OSM
©BD TOPO
©CLC

## Slide 16: State of the art – LU classification
Administrative Zoning
OSM Landuse polygons
Blocks from roads
Raster grids
Existing LU maps
Use of a wide variety of:
Data sources
Types of mapping unit
Vu et al. (2021), Hu et al. (2023)
R. Yang et al. (2025), Srivastava et al. (2019)
Du et al. (2021), Song et al. (2018), Wang et al. (2023), Sun et al. (2023), Wu et al. (2023), Zhang et al. (2017), Feng et al. (2023), He et al. (2021), Qin et al. (2022), Su et al. (2023), Yang et al. (2023), Li et al. (2023), Mawuenyegah et al. (2022)
C. Cao et al. (2019), Liu et al. (2022), R. Cao et al. (2018), Pei et al. (2014)
G. Zhu et al. (2025), Xu et al. (2023)

## Slide 17: State of the art – LU classification
    ⊝ Clusters not guaranteed to be meaningful LU classes nor to align with existing LU nomenclatures
    ⊕︀ No need for training datasets
    ⊕︀ Able to handle multiple sources
    ⊝ Requires expert knowledge
    ⊝ Difficult with several data sources
    ⊕︀ No need for training datasets
    ⊕︀ Explicit relationships between data sources and output classification
Use of a wide variety of:
    ⊝ Requires high quality training datasets
    ⊕︀ Aligned with a given LU nomenclature
    ⊕︀ Able to handle multiple sources
Introduction
State of the art
LU classification
Conclusion
LU change detection
Data sources
Types of mapping unit
Classification methods:
  Rule-based approaches: Jokar Arsanjani et al. (2013), Fonte et al. 2018), Song et al. (2018), Vu et al. (2021), Feng et al. (2023)
  Unsupervised classification (K-means, fuzzy C-means): Pei et al. (2014), Hu et al. (2023), Xu et al. (2023)
  Supervised classification (SVM, RF, GB, CNN, GNN, Transformers): Pan et al. (2013), Zhang et al. (2017), R. Cao et al. (2018), Srivastava et al., C. Cao et al., Zhu et al. (2019), Mao et al. (2020), Meng et al., Du et al., He et al. (2021), Deng et al., Mawuenyegah et al., Qin et al., Zheng et al., Liu et al. (2022), Wang et al., Sun et al., Wu et al., Su et al., Yang et al., Li et al. , Xu et al., Huang et al., Zhang et al. (2023), Lv et al., Yang et al., Zhu et al. (2025)

## Slide 18: Research questions
Which data sources are relevant for LU classification and change detection and why?
Which methods and strategies are most efficient for these tasks?
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 19: Positionning
Supervised machine learning approach for LU classification and change detection
Toward a better understanding of the contributions of the sources and the impact of their imperfections
Fusion of very heterogeneous data sources
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 20: LU classification
Methodology
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 21: General LU classification workflow
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: First choose

## Slide 22: Selection of ground truth LU maps
OCS GE LU maps produced by IGN:
INSPIRE compliant, interoperable with other European products
High resolution
High thematic precision
Strictly separate LU from LC
At least two vintages for each French department
Semi-automatic production
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: High precision
Two vintages are available for each French department

## Slide 23: Selection of ground truth LU maps
French departments of Gers (2019), Rhône (2020) and Essonne (2018 and 2021)
Heterogeneous study areas that present a diversity of rural and urban landscapes
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: High precision
Two vintages are available for each French department

## Slide 24: Selection of mapping units
Crucial because of the Modifiable Areal Unit Problem (Openshaw, 1983)
Less precise mapping units → LU mix within the mapping units
→ Less thematically precise nomenclatures
OCS GE polygons → from main networks, cadastral parcels, and LC data
Majority LU class within the mapping unit
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 25: Selection of geographic data sources for LU classification
Data sources that contain LU related information
Availability in France
FAIR principles (Findable, Accessible, Interoperable, Reusable) Wilkinson et al. (2016)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 26: Selection of geographic data sources - CLC
Land cover maps: CLC
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 27: Selection of geographic data sources - OSO
Land cover maps: CLC, OSO
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 28: Selection of geographic data sources - BD TOPO
Land cover maps: CLC, OSO
Topographic databases: BD TOPO
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 29: Selection of geographic data sources - RPG
Land cover maps: CLC, OSO
Topographic databases: BD TOPO, RPG
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 30: Selection of geographic data sources - OSM
Land cover maps: CLC, OSO
Topographic databases: BD TOPO, RPG, OSM
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 31: Selection of geographic data sources - Land Files
Land cover maps: CLC, OSO
Topographic databases: BD TOPO, RPG, OSM
Cadastral data: Land Files
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 32: Selection of geographic data sources - BD ORTHO
Land cover maps: CLC, OSO
Topographic databases: BD TOPO, RPG, OSM
Cadastral data: Land Files
Aerial images: BD Ortho
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 33: Selection of geographic data sources - INSEE
Land cover maps: CLC, OSO
Topographic databases: BD TOPO, RPG, OSM
Cadastral data: Land Files
Aerial images: BD Ortho
Socio-demographic statistics: INSEE
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 34: Selection of geographic data sources - Geometry
Land cover maps: CLC, OSO
Topographic databases: BD TOPO, RPG, OSM
Cadastral data: Land Files
Aerial images: BD Ortho
Socio-demographic statistics: INSEE
Geometry of the mapping units
Introduction
State of the art
LU classification
Conclusion
LU change detection
9 data sources of 6 types:

## Slide 35: Extraction of attributes
quantitative qualitative (categorical)
Introduction
State of the art
LU classification
Conclusion
LU change detection
"Number of residential buildings"
"Mean buildings height"
Several types of attributes depending on
  the geometry of the data source
  the data representation
  the scale relationship with the mapping units
  the explicitness of LU information
Formalized extraction process based on these types
Neighboring attributes
Hypotheses on their contribution to LU classification

## Slide 36: Extraction of attributes
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 37: Extraction of attributes – neighboring attributes
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 38: Extracted attributes
Type | Source | Number of attributes | Neighboring attributes
LU segmentation | OCS GE LU geometry | 25 | 25
Optical imagery | BD ORTHO | 8 | 8
LC classification | CLC | 1 | 1
 | OSO | 1 | 1
Topographic database | BD TOPO buildings | 17 | 17
 | BD TOPO other | 13 | 13
 | RPG | 1 | 1
 | OpenStreetMap | 36 | 36
Demographic data | INSEE | 6 | 6
Land Files | DGFIP | 18 | 18
Total |  | 252 | 
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 39: LU classification
Class balancing by minority classes synthetic oversampling: SMOTE-NC algorithm (Chawla et al., 2014)
Spatial and temporal transferability experiments
We showed in (Cubaud et al., 2023) that early fusion performed better than late fusion
XGBoost algorithm (Chen and Guestrin, 2016)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 40: Explainability
How individual predictions are made?
Impact and interactions of the sources and attributes?
What information is used for each class?
Model improvement
Handling uncertainty
Error diagnosis
Trust and transparency
Helps decision making
Relevance of sources and attributes
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 41: Explainability
3 complementary model-agnostic methods:
LA-1CO: Leave All minus one Covariate Out The model is trained and evaluated using only one data source.
  Standalone relevance of each data source
LOCO (J. Lei et al., 2018): Leave One Covariate Out The model is trained and evaluated using all sources except one.
  Added value and complementarity of the data sources
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: We chose to these methods because they are model agnostic and provide numerous interesting and complementary insights but we have to keep in mind to interpret them the known flaws and biases of these methods

## Slide 42: Explainability
Polygons
SHAP(k, X)
Polygons
SHAP(X)
Polygons
SHAP(i, k, X)
3 complementary model-agnostic methods:
SHAP (Lundberg & Lee, 2017): Shapley Additive exPlainations Quantifies the contribution of each attribute to the prediction of a class for a specific sample. → Local explanations (error diagnosis)
  Aggregation for per-class and global importance of the attributes.
Introduction
State of the art
LU classification
Conclusion
LU change detection
Attributes
Classes
Classes

## Slide 43: LU classification
Results
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 44: LU classification results
Study dataset | mF1 | OA
Gers (2019) | 83% | 88%
Rhône (2020) | 86% | 92%
Essonne (2018) | 85% | 94%
Essonne (2021) | 81% | 93%
Metrics per class for the Rhône dataset
Road Transport (LU4.1.1): F1= 94%
Public utility networks (LU4.3): F1= 61%
Introduction
State of the art
LU classification
Conclusion
LU change detection
Agriculture
Forestry
Extractive activities
Secondary production
Tertiary production
Road transport
Railway transport
Air transport
Public utility networks
Residential
Other

## Slide 45: Example of a misclassification
Aerodrome of Lyon – Brindas
Predicted tertiary production (LU3) instead of air transport (LU4.1.3)
BD Ortho, OCSGE © IGN
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 46: Example of a misclassification
Aerodrome of Lyon – Brindas
Predicted tertiary production (LU3) instead of air transport (LU4.1.3)
Information given by the sources:
Aerodrome in BD TOPO and OSM
Undifferentiated buildings in BD TOPO and one commercial building
In land files the area is considered as tertiary
BD Ortho, OCSGE © IGN
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 47: Example of a misclassification
Polygon Aerodrome of Lyon – Brindas
True class : Air transport (LU4.1.3)
Badly predicted class : Tertiary production (LU3)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 48: Example of a misclassification
Polygon Aerodrome of Lyon – Brindas
True class : Air transport (LU4.1.3)
Badly predicted class : Tertiary production (LU3)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 49: Example of a misclassification
Polygon Aerodrome of Lyon – Brindas
Base probability LU3 = 13.1%
Base logits LU3 = 0.36
Base probability LU4.1.3 = 0.08%
Base logits LU4.1.3 = -4.71
log(p) +cst
True class : Air transport (LU4.1.3)
Badly predicted class : Tertiary production (LU3)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 50: Example of a misclassification
Polygon Aerodrome of Lyon – Brindas
Base probability LU3 = 13.1%
Base logits LU3 = 0.36
= 1.35
Base probability LU4.1.3 = 0.08%
Base logits LU4.1.3 = -4.71
= 2.19
log(p) +cst
True class : Air transport (LU4.1.3)
Badly predicted class : Tertiary production (LU3)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 51: Example of a misclassification
Polygon Aerodrome of Lyon – Brindas
Base probability LU3 = 13.1%
Base logits LU3 = 0.36
= 1.35
Final logits = 1.71
Probability LU3 = 91%
Base probability LU4.1.3 = 0.08%
Base logits LU4.1.3 = -4.71
= 2.19
Final logits = -2.59
Probability LU4.1.3 = 1.31%
log(p) +cst
softmax
True class : Air transport (LU4.1.3)
Badly predicted class : Tertiary production (LU3)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 52: Link between attributes and classes
Links between the 15 most important attributes and the LU classes
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: Links between the 15 most important attributes and the LU classes

## Slide 53: Link between attributes and classes
Links between the 15 most important attributes and the LU classes
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: Links between the 15 most important attributes and the LU classes

## Slide 54: Link between attributes and classes
All the sources have at least one attribute among the 50 most important attributes
→ usefulness of multi source classification
Introduction
State of the art
LU classification
Conclusion
LU change detection
Notes: Links between the 15 most important attributes and the LU classes

## Slide 55: LU classification results
Individual study area classification
Transferability
Study dataset | mF1
Gers (2019) | 83%
Rhône (2020) | 86%
Essonne (2018) | 85%
Essonne (2021) | 81%
Study dataset | mF1
Gers to Rhône | 50%
Rhône to Gers | 51%
Essonne 2018 to 2021 | 75%
Essonne 2021 to 2018 | 80%
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 56: Transferability from Gers to Rhône
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 57: LU classification results
Individual study area classification
Transferability
Mixed train set transferability (80% of origin dataset and 5% of target dataset)
Study dataset | mF1
Gers (2019) | 83%
Rhône (2020) | 86%
Essonne (2018) | 85%
Essonne (2021) | 81%
Study dataset | mF1
Gers to Rhône | 50%
Rhône to Gers | 51%
Essonne 2018 to 2021 | 75%
Essonne 2021 to 2018 | 80%
Study dataset | mF1
Gers to Rhône | 70%
Rhône to Gers | 79%
Essonne 2018 to 2021 | 88%
Essonne 2021 to 2018 | 88%
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 58: LU change detection
Methodology
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 59: State of the art – Change detection
Mostly remote-sensing-based LC change detection (Gonthier, 2025)
  CNN-based models
  Often Siamese Embedding-level fusion architectures (Daudt et al., 2018)
LU change detection remains mostly unstudied
  Difficulties:
  heterogeneity and rarity of LU changes
  heterogeneous multi-source change detection
  semantic and geometric changes
  C. Cao et al. (2019), Olteanu-Raimond et al. (2020), L. Liu et al. (2021), Yao et al. (2023), S. Shi et al. (2025), Fang et al. (2025)
  Lack of a high quality LU change ground truth
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 60: General LU change detection workflow
Context of the update of an LU map
Same steps as in LU classification
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 61: Construction of a LU change ground truth
Create a ground truth of the ti polygons that change their LU:
Semantic changes
Geometric changes
LU ti
LU ti+1
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 62: Construction of a LU change ground truth
Intersection between the two GT LU maps
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 63: Construction of a LU change ground truth
Intersection between the two GT LU maps
LU change of the intersection polygons
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 64: Construction of a LU change ground truth
Intersection between the two GT LU maps
LU change of the intersection polygons
Type of geometric change
(Thériault & Claramunt, 1999)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 65: Construction of a LU change ground truth
Intersection between the two GT LU maps
LU change of the intersection polygons
Type of geometric change
Changing ti polygons
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 66: Construction of a LU change ground truth
Intersection between the two GT LU maps
LU change of the intersection polygons
Type of geometric change
Changing ti polygons
Manual verifications and corrections
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 67: Construction of a LU change ground truth
Example of correction
LU6.3 Without use
LU4.1.2 Railway transport
Introduction
State of the art
LU classification
Conclusion
LU change detection
Verification of 816 polygons
"LU change, no geometric change"
Modification of 668 of them
Actually no LU change

## Slide 68: LU change ground truth of Essonne between 2018 and 2021
Polygons | Changed LU | Did not changed LU
Number | 3,926 | 197,163
Percentage | 2% | 98%
81% change LC
19% did not change LC
54% of LC changes are not LU changes
Introduction
State of the art
LU classification
Conclusion
LU change detection
In terms of surface area, a larger proportion (22%) of the study area has changed LU ↑ large polygons of which only a small part changed

## Slide 69: Example of LU change dilution
Agriculture
Tertiary production
Agriculture
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 70: How LU classes evolved between 2018 and 2021?
Introduction
State of the art
LU classification
Conclusion
LU change detection
A large number of pairs of LU classes
Some are very rare
Mixed LU resulting from the use of ti mapping units
These mixed LU are also very heterogeneous
Makes learning LU changes very difficult
2018 LU Class
2021 LU Class

## Slide 71: LU change detection
Goal: Detect ti mapping units which LU have change
Inputs: attributes extracted from the data sources at ti and ti+1 in the ti mapping units.
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 72: LU change detection
3 possible data fusion approaches for the attributes of the two dates:
  Post-classification
  Embedding-level fusion
  Early fusion
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 73: LU change detection
Results
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 74: LU change detection results
Post classification approach: mF1=56%, F1change=18%
Accurate but not perfect LU classification → numerous false detections of LU changes
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 75: LU change detection results
Embedding level fusion approach: mF1=67%, F1change=35%
Adding LU classification constraints: mF1=70%, F1change=41%
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 76: LU change detection results
Early fusion approach: mF1=74%, F1change=49%
45% of the LU changes are detected
55% of the detections are real LU changes
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 77: LU change detection examples
ti+1 (2021)
ti (2018)
Accurate change detection
Introduction
State of the art
LU classification
Conclusion
LU change detection
LU5: Residential, LU4.1.1: Road Transport
Detected polygon
Geometric change

## Slide 78: LU change detection examples
ti+1 (2021)
ti (2018)
False detection
Introduction
State of the art
LU classification
Conclusion
LU change detection
LU5: Residential
Detected polygon
Geometric change

## Slide 79: Conclusion
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 80: Contributions
Formalization of the extraction of attributes from data sources containing LU information
General workflow for LU classification
Formalization of LU changes (semantic + geometric changes)
Comparison of approaches for LU change detection
Explainability methodology applied to LU classification and change detection
Publication of datasets to serve as benchmark for LU classification
Formalization of the extraction of attributes from data sources containing LU information
General workflow for LU classification
Formalization of LU changes (semantic + geometric changes)
Comparison of approaches for LU change detection
Explainability methodology applied to LU classification and change detection
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 81: Publications
Journal
Cubaud, M., Le Bris, A., Jolivet, L., and Olteanu-Raimond, A. M. (2024). Assessing the transferability of a multi-source land use classification workflow across two heterogeneous urban and rural areas. International Journal of Digital Earth, 17(1). https://doi.org/10.1080/17538947.2024.2376274
International conferences
Cubaud, M., Le Bris, A., Jolivet, L., and Olteanu-Raimond, A.-M. (2023). Comparison of two data fusion approaches for land use classification, Int. Arch. Photogramm. Remote Sens. Spatial Inf. Sci., XLVIII-1/W2-2023, 699–706, https://doi.org/10.5194/isprs-archives-XLVIII-1-W2-2023-699-2023, 2023.
Cubaud, M., Le Bris, A., Jolivet, L., and Olteanu-Raimond, A. M. (2025). Interpretability of a multi-source Land Use classification machine learning model using a SHAP approach, International Conference on Spatial Analysis and GEOmatics (SAGEO 2025)
Future publications
Cubaud, M., Olteanu-Raimond, A-M., Fonte, C., Duarte, D., Estima, J., See, L., Gonthier, N., Jolivet, L., Mallet, C., Le Bris, A., Vyron, A.: OntoLULC-SOTA: An ontology based approach to make systematic reviews for LULC data, ISPRS 2026 (submitted)
Datasets
Cubaud, M., Le Bris, A., Jolivet, L., Olteanu-Raimond, A.-M., & Institut national de l'information géographique et forestière. (2024). OCS GE Land Use dataset including the French departments of Gers and Rhône. Zenodo. https://doi.org/10.5281/zenodo.10462844
Code
https://github.com/mcubaud/multi-source-Land-Use-classification
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 82: Perspectives
Better integration of remote sensing information
Classification of mixed LU
Improving LU change detection ground truths
Extension of the methodology to other products
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 83: Perspectives
Better integration of remote sensing information
Classification of mixed LU
Improving LU change detection ground truths
Extension of the methodology to other products
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 84: Improve LU change detection ground truths
Using crowdsourcing campaigns to validate LU changes (L. Liu et al., 2021)
Using automatic label noise detection approaches (Liang et al., 2022)
Increasing the variety by using several study areas or by generating synthetic changes (Benidir et al., 2025)
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 85: Perspectives
Better integration of remote sensing information
Improving LU change detection ground truths
Classification of mixed LU
Extension of the methodology to other products
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 86: Better integration of remote sensing information
FLAIR (Garioud et al., 2022) U-Net trained for LC
Encoder
Decoder
Raster LC
Classification
Intersection with LU mapping units
Extraction of attributes for LU classification or LU change detection
Feature maps
Introduction
State of the art
LU classification
Conclusion
LU change detection
Fine tune for LU classification or LU change detection

## Slide 87: Perspectives
Better integration of remote sensing information
Extension of the methodology to other products
Classification of mixed LU
Improving LU change detection ground truths
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 88: Extension of the methodology to other products
Urban Atlas
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 89: Perspectives
Better integration of remote sensing information
Extension of the methodology to other products
Classification of mixed LU
Improving LU change detection ground truths
Introduction
State of the art
LU classification
Conclusion
LU change detection

## Slide 90: Classification of mixed LU
Different types of LU mix
Limit to the hypothesis of a majority LU
No existing mixed LU dataset in France
Creation of synthetic datasets?
Vertical mix
©panoramax
Horizontal mix
Introduction
State of the art
LU classification
Conclusion
LU change detection
On the same place

## Slide 91: Publications
Thank you for your attention!
Introduction
State of the art
LU classification
Conclusion
LU change detection